# Extended Asm - Assembler Instructions with C Expression Operands
With extended asm you can read and write C variables from assembler and perform jumps from assembler code to C labels. Extended asm syntax uses colons (‘:’) to delimit the operand parameters after the assembler template:
     asm [volatile] ( AssemblerTemplate
        : OutputOperands
        [ : InputOperands
        [ : Clobbers ] ])

The asm keyword is a GNU extension. When writing code that can be compiled with -ansi and the various -std options, use __asm__ instead of asm (see Alternate Keywords).
## Qualifiers
volatile
The typical use of extended asm statements is to manipulate input values to produce output values. However, your asm statements may also produce side effects. If so, you may need to use the volatile qualifier to disable certain optimizations. See Volatile.
## Parameters
AssemblerTemplate
This is a literal string that is the template for the assembler code. It is a combination of fixed text and tokens that refer to the input, output, and goto parameters. See AssemblerTemplate.
OutputOperands
A comma-separated list of the C variables modified by the instructions in the AssemblerTemplate. An empty list is permitted. See OutputOperands.
InputOperands
A comma-separated list of C expressions read by the instructions in the AssemblerTemplate. An empty list is permitted. See InputOperands.
Clobbers
A comma-separated list of registers or other values changed by the AssemblerTemplate, beyond those listed as outputs. An empty list is permitted. See Clobbers.
GotoLabels
When you are using the goto form of asm, this section contains the list of all C labels to which the code in the AssemblerTemplate may jump. See GotoLabels.
asm statements may not perform jumps into other asm statements, only to the listed GotoLabels. GCC's optimizers do not know about other jumps; therefore they cannot take account of them when deciding how to optimize.
The total number of input + output + goto operands is limited to 30.
## Input Operands
Input operands make values from C variables and expressions available to the assembly code.
Operands are separated by commas. Each operand has this format:
     [ [asmSymbolicName] ] constraint (cexpression)
asmSymbolicName
Specifies a symbolic name for the operand. Reference the name in the assembler template by enclosing it in square brackets (i.e. ‘%[Value]’). The scope of the name is the asm statement that contains the definition. Any valid C variable name is acceptable, including names already defined in the surrounding code. No two operands within the same asm statement can use the same symbolic name.
When not using an asmSymbolicName, use the (zero-based) position of the operand in the list of operands in the assembler template. For example if there are two output operands and three inputs, use ‘%2’ in the template to refer to the first input operand, ‘%3’ for the second, and ‘%4’ for the third.
constraint
A string constant specifying constraints on the placement of the operand; See Constraints, for details.
Input constraint strings may not begin with either ‘=’ or ‘+’. When you list more than one possible location (for example, ‘"irm"’), the compiler chooses the most efficient one based on the current context. If you must use a specific register, but your Machine Constraints do not provide sufficient control to select the specific register you want, local register variables may provide a solution (see Local Register Variables).
Input constraints can also be digits (for example, "0"). This indicates that the specified input must be in the same place as the output constraint at the (zero-based) index in the output constraint list. When using asmSymbolicName syntax for the output operands, you may use these names (enclosed in brackets ‘[]’) instead of digits.
cexpression
This is the C variable or expression being passed to the asm statement as input. The enclosing parentheses are a required part of the syntax.
When the compiler selects the registers to use to represent the input operands, it does not use any of the clobbered registers (see Clobbers).
If there are no output operands but there are input operands, place two consecutive colons where the output operands would go:
     __asm__ ("some instructions"
        : /* No outputs. */
        : "r" (Offset / 8));
Warning: Do not modify the contents of input-only operands (except for inputs tied to outputs). The compiler assumes that on exit from the asm statement these operands contain the same values as they had before executing the statement. It is not possible to use clobbers to inform the compiler that the values in these inputs are changing. One common work-around is to tie the changing input variable to an output variable that never gets used. Note, however, that if the code that follows the asm statement makes no use of any of the output operands, the GCC optimizers may discard the asm statement as unneeded (see Volatile).
asm supports operand modifiers on operands (for example ‘%k2’ instead of simply ‘%2’). Typically these qualifiers are hardware dependent. The list of supported modifiers for x86 is found at x86 Operand modifiers.
In this example using the fictitious combine instruction, the constraint "0" for input operand 1 says that it must occupy the same location as output operand 0. Only input operands may use numbers in constraints, and they must each refer to an output operand. Only a number (or the symbolic assembler name) in the constraint can guarantee that one operand is in the same place as another. The mere fact that foo is the value of both operands is not enough to guarantee that they are in the same place in the generated assembler code.
     asm ("combine %2, %0"
        : "=r" (foo)
        : "0" (foo), "g" (bar));
Here is an example using symbolic names.
     asm ("cmoveq %1, %2, %[result]"
        : [result] "=r"(result)
        : "r" (test), "r" (new), "[result]" (old));
## Clobbers
While the compiler is aware of changes to entries listed in the output operands, the inline asm code may modify more than just the outputs. For example, calculations may require additional registers, or the processor may overwrite a register as a side effect of a particular assembler instruction. In order to inform the compiler of these changes, list them in the clobber list. Clobber list items are either register names or the special clobbers (listed below). Each clobber list item is a string constant enclosed in double quotes and separated by commas.
Clobber descriptions may not in any way overlap with an input or output operand. For example, you may not have an operand describing a register class with one member when listing that register in the clobber list. Variables declared to live in specific registers (see Explicit Register Variables) and used as asm input or output operands must have no part mentioned in the clobber description. In particular, there is no way to specify that input operands get modified without also specifying them as output operands.
When the compiler selects which registers to use to represent input and output operands, it does not use any of the clobbered registers. As a result, clobbered registers are available for any use in the assembler code.
Here is a realistic example for the VAX showing the use of clobbered registers:
     asm volatile ("movc3 %0, %1, %2"
        : /* No outputs. */
        : "g" (from), "g" (to), "g" (count)
        : "r0", "r1", "r2", "r3", "r4", "r5");
Also, there are two special clobber arguments:
"cc"
The "cc" clobber indicates that the assembler code modifies the flags register. On some machines, GCC represents the condition codes as a specific hardware register; "cc" serves to name this register. On other machines, condition code handling is different, and specifying "cc" has no effect. But it is valid no matter what the target.
"memory"
The "memory" clobber tells the compiler that the assembly code performs memory reads or writes to items other than those listed in the input and output operands (for example, accessing the memory pointed to by one of the input parameters). To ensure memory contains correct values, GCC may need to flush specific register values to memory before executing the asm. Further, the compiler does not assume that any values read from memory before an asm remain unchanged after that asm; it reloads them as needed. Using the "memory" clobber effectively forms a read/write memory barrier for the compiler.
Note that this clobber does not prevent the processor from doing speculative reads past the asm statement. To prevent that, you need processor-specific fence instructions.
Flushing registers to memory has performance implications and may be an issue for time-sensitive code. You can use a trick to avoid this if the size of the memory being accessed is known at compile time. For example, if accessing ten bytes of a string, use a memory input like:
{"m"( ({ struct { char x[10]; } *p = (void *)ptr ; *p; }) )}.
# Constraints for asm Operands
## Simple Constraints
The simplest kind of constraint is a string full of letters, each of which describes one kind of operand that is permitted. Here are the letters that are allowed:
whitespace
Whitespace characters are ignored and can be inserted at any position except the first. This enables each alternative for different operands to be visually aligned in the machine description even if they have different number of constraints and modifiers.
‘m’
A memory operand is allowed, with any kind of address that the machine supports in general. Note that the letter used for the general memory constraint can be re-defined by a back end using the TARGET_MEM_CONSTRAINT macro.
‘o’
A memory operand is allowed, but only if the address is offsettable. This means that adding a small integer (actually, the width in bytes of the operand, as determined by its machine mode) may be added to the address and the result is also a valid memory address.
For example, an address which is constant is offsettable; so is an address that is the sum of a register and a constant (as long as a slightly larger constant is also within the range of address-offsets supported by the machine); but an autoincrement or autodecrement address is not offsettable. More complicated indirect/indexed addresses may or may not be offsettable depending on the other addressing modes that the machine supports.
Note that in an output operand which can be matched by another operand, the constraint letter ‘o’ is valid only when accompanied by both ‘<’ (if the target machine has predecrement addressing) and ‘>’ (if the target machine has preincrement addressing).
‘V’
A memory operand that is not offsettable. In other words, anything that would fit the ‘m’ constraint but not the ‘o’ constraint.
‘<’
A memory operand with autodecrement addressing (either predecrement or postdecrement) is allowed. In inline asm this constraint is only allowed if the operand is used exactly once in an instruction that can handle the side-effects. Not using an operand with ‘<’ in constraint string in the inline asm pattern at all or using it in multiple instructions isn't valid, because the side-effects wouldn't be performed or would be performed more than once. Furthermore, on some targets the operand with ‘<’ in constraint string must be accompanied by special instruction suffixes like %U0 instruction suffix on PowerPC or %P0 on IA-64.
‘>’
A memory operand with autoincrement addressing (either preincrement or postincrement) is allowed. In inline asm the same restrictions as for ‘<’ apply.

‘r’
A register operand is allowed provided that it is in a general register.
‘i’
An immediate integer operand (one with constant value) is allowed. This includes symbolic constants whose values will be known only at assembly time or later.
‘n’
An immediate integer operand with a known numeric value is allowed. Many systems cannot support assembly-time constants for operands less than a word wide. Constraints for these operands should use ‘n’ rather than ‘i’.
‘I’, ‘J’, ‘K’, ... ‘P’
Other letters in the range ‘I’ through ‘P’ may be defined in a machine-dependent fashion to permit immediate integer operands with explicit integer values in specified ranges. For example, on the 68000, ‘I’ is defined to stand for the range of values 1 to 8. This is the range permitted as a shift count in the shift instructions.
‘E’
An immediate floating operand (expression code const_double) is allowed, but only if the target floating point format is the same as that of the host machine (on which the compiler is running).
‘F’
An immediate floating operand (expression code const_double or const_vector) is allowed.
‘G’, ‘H’
‘G’ and ‘H’ may be defined in a machine-dependent fashion to permit immediate floating operands in particular ranges of values.
‘s’
An immediate integer operand whose value is not an explicit integer is allowed.
This might appear strange; if an insn allows a constant operand with a value not known at compile time, it certainly must allow any known value. So why use ‘s’ instead of ‘i’? Sometimes it allows better code to be generated.
For example, on the 68000 in a fullword instruction it is possible to use an immediate operand; but if the immediate value is between −128 and 127, better code results from loading the value into a register and using the register. This is because the load into the register can be done with a ‘moveq’ instruction. We arrange for this to happen by defining the letter ‘K’ to mean “any integer outside the range −128 to 127”, and then specifying ‘Ks’ in the operand constraints.
‘g’
Any register, memory or immediate integer operand is allowed, except for registers that are not general registers.

‘X’
Any operand whatsoever is allowed.
‘0’, ‘1’, ‘2’, ... ‘9’
An operand that matches the specified operand number is allowed. If a digit is used together with letters within the same alternative, the digit should come last.
This number is allowed to be more than a single digit. If multiple digits are encountered consecutively, they are interpreted as a single decimal integer. There is scant chance for ambiguity, since to-date it has never been desirable that ‘10’ be interpreted as matching either operand 1 or operand 0. Should this be desired, one can use multiple alternatives instead.
This is called a matching constraint and what it really means is that the assembler has only a single operand that fills two roles which asm distinguishes. For example, an add instruction uses two input operands and an output operand, but on most CISC machines an add instruction really has only two operands, one of them an input-output operand:
        addl #35,r12
Matching constraints are used in these circumstances. More precisely, the two operands that match must include one input-only operand and one output-only operand. Moreover, the digit must be a smaller number than the number of the operand that uses it in the constraint.
‘p’
An operand that is a valid memory address is allowed. This is for “load address” and “push address” instructions.
‘p’ in the constraint must be accompanied by address_operand as the predicate in the match_operand. This predicate interprets the mode specified in the match_operand as the mode of the memory reference for which the address would be valid.
other-letters
Other letters can be defined in machine-dependent fashion to stand for particular classes of registers or other arbitrary operand types. ‘d’, ‘a’ and ‘f’ are defined on the 68000/68020 to stand for data, address and floating point registers.
## Multiple Alternative Constraints
Sometimes a single instruction has multiple alternative sets of possible operands. For example, on the 68000, a logical-or instruction can combine register or an immediate value into memory, or it can combine any kind of operand into a register; but it cannot combine one memory location into another.
These constraints are represented as multiple alternatives. An alternative can be described by a series of letters for each operand. The overall constraint for an operand is made from the letters for this operand from the first alternative, a comma, the letters for this operand from the second alternative, a comma, and so on until the last alternative. All operands for a single instruction must have the same number of alternatives.
So the first alternative for the 68000's logical-or could be written as "+m" (output) : "ir" (input). The second could be "+r" (output): "irm" (input). However, the fact that two memory locations cannot be used in a single instruction prevents simply using "+rm" (output) : "irm" (input). Using multi-alternatives, this might be written as "+m,r" (output) : "ir,irm" (input). This describes all the available alternatives to the compiler, allowing it to choose the most efficient one for the current conditions.
There is no way within the template to determine which alternative was chosen. However you may be able to wrap your asm statements with builtins such as __builtin_constant_p to achieve the desired results.
## Constraint Modifier Characters
Here are constraint modifier characters.
‘=’
Means that this operand is written to by this instruction: the previous value is discarded and replaced by new data.
‘+’
Means that this operand is both read and written by the instruction.
When the compiler fixes up the operands to satisfy the constraints, it needs to know which operands are read by the instruction and which are written by it. ‘=’ identifies an operand which is only written; ‘+’ identifies an operand that is both read and written; all other operands are assumed to only be read.
If you specify ‘=’ or ‘+’ in a constraint, you put it in the first character of the constraint string.
‘&’
Means (in a particular alternative) that this operand is an earlyclobber operand, which is written before the instruction is finished using the input operands. Therefore, this operand may not lie in a register that is read by the instruction or as part of any memory address.
‘&’ applies only to the alternative in which it is written. In constraints with multiple alternatives, sometimes one alternative requires ‘&’ while others do not. See, for example, the ‘movdf’ insn of the 68000.
A operand which is read by the instruction can be tied to an earlyclobber operand if its only use as an input occurs before the early result is written. Adding alternatives of this form often allows GCC to produce better code when only some of the read operands can be affected by the earlyclobber. See, for example, the ‘mulsi3’ insn of the ARM.
Furthermore, if the earlyclobber operand is also a read/write operand, then that operand is written only after it's used.
‘&’ does not obviate the need to write ‘=’ or ‘+’. As earlyclobber operands are always written, a read-only earlyclobber operand is ill-formed and will be rejected by the compiler.
‘%’
Declares the instruction to be commutative for this operand and the following operand. This means that the compiler may interchange the two operands if that is the cheapest way to make all operands fit the constraints. ‘%’ applies to all alternatives and must appear as the first character in the constraint. Only read-only operands can use ‘%’.
GCC can only handle one commutative pair in an asm; if you use more, the compiler may fail. Note that you need not use the modifier if the two alternatives are strictly identical; this would only waste time in the reload pass.